## Slide 1: MODFLOW-OWHM v2 Features and Updates The next generation in fully integrated hydrologic simulation software
April 12th, 2016
Scott E. Boyce and Randall T. Hanson
California Water Science Center
U.S. Department of the Interior
U.S. Geological Survey
seboyce@usgs.gov

## Slide 2: MODFLOW And Its Children
The MODFLOW-2005 (MF) family of hydrologic simulators has diverged into multiple versions designed for specific needs.
This divergence, while creating more options, also created more limitations.
  With the selection of one version meant that the features of another were not available.
Notes: Even many small/undocumented versions or state/project versions.

## Slide 3: MODFLOW-OWHM One-Water Hydrologic Flow Model
The One-Water Hydrologic Flow Model, MF-OWHM, is an enhanced fusion of multiple MF versions to serve as a new integrated hydrologic flow modeling software.
MF05 FMP RIP SWI SWR NWT LGR
OWHM
One Water
Notes: CFP and more for future

## Slide 4: Current Package Support
BAS | ETS | HUF | MNW2 | RES | SWT
BCF | EVT | HYD | MNWI | RIP | UPW
BFH | FHB | IBS | MULT | RIV | UZF
CHD | FMP | KDEP | NWT | RVOB | WEL
CHOB | GAGE | LAK | OBS | SFR | ZONE
DE4 | GBOB | LGR | OC | SIP | 
DIS | GHB | LMT | PCG | STR | SWO
DRN | GMG | LPF | PCGN | SUB | SUS
DROB | HFB | LVDA | PVAL | SWI | SSUB
DRT | HOB | MNW1 | RCH | SWR | CFP
Notes: Technically all packages were modified slightly for speed improvement.
They are still backward compatible with MF05, future add CFP with Thomas Reimann, SWO
DIS –REALTIM/COORD HFB –Vertical Barrier/RP
Tabfiles and ExpressionParser
Tested against all example problems

## Slide 5
Current MODFLOW-OWHM (One-Water Hydrologic Model)
MF-OWHM Features (v1):
Solvers (NWT, PCG, PCGN, GMG, SIP, D4)
Surface-water (SWR, SFR, LAK) + Linkages to Runoff Models (BCM,VIC, PRMS)
Landscape (FMP3)
Evapotranspiration (ET, ETS, RIP-ET, FMP3)
Drains (DRN, DRT  FMP/SFR/SWR connection for Tile Drains & Water Reuse)
Aquifers (LPF, UPW, HUF)
Wells (Well, FMP-well, MNW1, MNW2  FMP connection)
Boundary Flows (GHB, FHB) GHB-TabFiles
Deformation (SUB, SUB-WT)
Seawater Intrusion (SWI)
Embedded Models (LGR)
Flow Barriers (HFB2  variable faults/layer connections)
Unsaturated Flow (UZF, SFR, SWR)
Time Series (HYDMOD, SFR-Gage, SWR-Obs)
New Support Features:
Deformation Linkage (SUB-Link)  All land-surface/aquifer features
Expression Parser (MULT2)  Equations for Aquifer and Subsidence Parm’s
MT3D Output  SFR, UZF, additional features
Additional I/O for Parameter Estimation OBS & Optimization Analysis (GWM)
Ongoing Development (MF-OWHM v2):
Reservoir Linkage to SFR/SWR/FMP  USBR contribution
Adjacent Model Linkage (LGR), Multi-Model Simulation, Ag MgmtGWM-FMP Link (Wells/Allot.)
FMP Linkage to Remote Sensing Data streams  Self-Updating Models
Improved and combined Subsidence Package, more complete MT3D linkages

## Slide 6: One Water Models In Development and Use

## Slide 7: Water Systems are Coupled
The interaction between different waters make a more complete simulation of conjunctive use
This provides better understanding of a water systems and how to manage it.
Simulation is more than connections of buckets that dump into each other.
  Simulation of conveyance is important!
  Systems reach a Rate Limit before a Volume Limited
  Paper Water versus Wet Water
Notes:     (wells take from rivers, runoff feeds the revers)

## Slide 8
Seepage in vineyard on right bank of San Joaquin River during high flows (4/13/2011)
San Joaquin River Restoration Project
Notes: Unintended effects by not looking at a fully coupled system. A restored river raised the gw table which caused an adjacent ag land to flood.

## Slide 9: Variable Water Balance Regions
Surface and Groundwater Allotments
Notes: Link to land use models and sustainability analysis.
Farms, Break E and T, Climate, Crop Coefficients
Currently assumes irrigation is well managed so it has steady state soil moisture because this is not an irrigation scheduler.
Also when you have time steps greater than a week soil mosture plays a smaller role than other water bearing bodies.
Despite this, a soil moisture package will be added in the future do to it being requested.

## Slide 10
One Water and the Farm Process
SUMMARY OF FEATURES AND ADVANTAGES
MODEL FEATURES MADE EASY
Estimates Irrigation Demand
Estimates Surface-Water Deliveries
Estimates Ground-water Pumpage
Estimates Net Recharge
Estimates all Components for ET, Runoff, and Deep Percolation
Complete Linkage to Ground-water and Surface-water Flow
ADVANTAGES FOR MODELERS
No need for indirect estimates of Pumpage, Recharge, ET, Runoff, or Surface-water deliveries
Uses Natural Data → Easy to Update Model
Saves time and money for constructing, operating, and updating models
Facilitates Operational and Forecasting Simulations

## Slide 11: Surface Water Operations Module (SWO)
Reservoir operations linkage Option
  Can link to FMP for dynamic supply and demand reservoir releases.
Simulates a Reservoir releases
  Demand Driven, Supply Constrained
  Calculates gains and losses along the river network
    Adjusts supply (ie releases) to ensure demanded water is met
  Paper Water versus Wet Water
  Storage available

## Slide 12
GW/SW Feedbacks
Bigger picture includes two-way feedbacks within Demand-Driven and Supply-Constrained Coupling
Surface Water
Storage / Allocation
Release / Delivery
Groundwater
Allotment / Right Pumping Rates
Landscape Consumptive Water Demand
Diversion
Pumping
Stream Flow
Aquifer Storage
GW Discharge
GW Head
SW Head
SW Seepage

## Slide 13
Reservoir
SFR Network
New Mexico
Texas
Mexico
Stream Flow Routing (SFR):
478 Segments
6,344 reaches
16 Inflow locations
71 Diversion Points
20 to 30% Water reuse as
part of the operating agreement

## Slide 14: Super Subsidence Package (SSUB)
A new subsidence package is under development for MF-OWHM
It represents a fusion between the predecessor packages with additional features and enhancements.
Think of the Nintendo (awesome) versus Super Nintendo (absolutely amazing)

## Slide 15: Overview of Subsidence Packages
SSUB





Simulation Feature | SUB | SUB-WT
3D regional flow and subsidence |  | 
Variable geostatic loads |  | 
Hydrodynamic lag |  | 
Stress-dependent storage properties |  | 
Stress-dependent hydraulic conductivity |  | 

## Slide 16: Subsidence
Completely rewritten computer code following Fortran 2003/2008 standard
  Improved vectorization/computational speed
  Better input file design
Define 4 types of interbeds
  Instantaneous Confine (normal SUB interbed)
  Delayed Confine (delayed SUB interbed)
  Instantaneous Stress (normal SUB-WT interbed)
  Delayed Stress (new, delayed SUB-WT interbed)

## Slide 17: New Features In Subsidence
  Subsidence Drive Deformation Dependent Flow.
  Deforms the Interbed Thickness
      Effects: Skeletal Storage Coefficient
  Deforms the model grid itself.
      Effects: Conductance and Storage Coefficient.
Delay interbeds will have a stress dependent vertical hydraulic conductivity option

## Slide 18
Notes: Not pictured here, but you could get unsaturated flow with UZF.

## Slide 19
Notes: Even many small/undocumented versions or state/project versions.

## Slide 20: New Features In Subsidence
Changing in time option for the above model Geostatic Load (Total Stress)
Input will accept porosity as a surrogate to the void ratio
Optional user-specified deformation from below model grid
Interbed and confining layers have separate budgets (files and blocks in List file)
Gravity observations
  Calculate gravity change as a result of compaction

## Slide 21: Characterization of karst systems (CFPv3)
strong heterogeneity
anisotropy
highly variable, non-linear flow
Questions:
storage?
flow behavior?
vulnerability?
…
Notes: Fractured Rock – Dual Porosity

## Slide 22
Numerical hybrid flow model
head dependent water transfer between matrix and conduits
MODFLOW-OWHM Conduit Flow Process (CFP) hydraulics
flow equations
matrix: 3D groundwater flow (Darcy)
pipes: 1D pipe flow (Darcy-Weisbach)
laminar: Hagen-Poiseuille
turbulent: Colebrook-White
(MODFLOW-OWHM)

## Slide 23: Partially Filled Pipe and Hydraulic Properties

## Slide 24
Improvements over MODFLOW-CFP
MODFLOW-OWHM Conduit Flow Process
(MODFLOW-OWHM)
Additional boundary conditions for pipes:
fixed head that can switch to limited flow (Bauer et al. 2005)
river (Cauchy type)
well (Neumann type)
input of time series
Additional storage for pipes:
Notes: Delayed Yield Feature

## Slide 25
General MODFLOW-OWHM Improvements
Coordinate System → Linked to other packages so you can reference location by X,Y coordinate rather than Row and Column.
Real Time (DIS) → Option to take into account leap years instead of using 365.2425 days in a year.
Calendar Dates (DIS) → Option to incorporate calendar dates.
ExpressionParser → Can now handle conditional evaluation in the form: IF(Condition, True, False). For example: IF(A<B, X^2, 4*X)
WEL Package → Rewritten using modern coding techniques. Can run old WEL code along with the new giving two WEL budget print outs (allows segmentation of budget information). New WEL pakage contains additional features such as emulation of pumpage reduction.
HFB → Now allows vertical flow barriers between model layers.

## Slide 26: Tabfile Improvements (Time Series Input)
Linked to the ExpressionParser → Tabfile no longer limited to just a single scale factor. Can be any expression that uses the tabfile value as the independent variable. Below is an example of a GHB parameter that uses the tabfile GHB_SLV and applies its result to the expression TABEXP:
GHB_SLV_1 GHB 1.0 153
1 30 67 -999. 55.12 GHB_SLV 1.0 " 0.450 + 1.025*TAB "
#Lay Row Col Bhead Cond TABNAM TSFAC TABEXP
Stress Period Time Frame → Time frame for processing tabfile values can be changed from being based on the current time step to the stress period.
Step Function → Option to disable interpolation when there is no data within time step and just use the previously available tabfile value. Useful for migration of older MODFLOW Input files as a first step to MF-OWHM.

## Slide 27: New Input Option: Line Feed
Input design can be used to replace entirely certain packages (WEL) or work along side the current input (MNW2).
Each input is called a feed file and can easily be made in Excel.
Below is an example Feed:
# Comments |  |  |  | Well
1 | 3 | 4 |  | W1
1 | 7 | 3 |  | W2
1 | 6 | 7 |  | W3
1 | 5 | 5 |  | W4
STRESS PERIOD |  |  |  | 
# W1 | W2 | W3 | W4 | SP
-1000 | 0.0 | -4500 | NaN | # 1
-500 | -1000 | -3000 | NaN | # 2
-1000 | -1500 | -1500 | NaN | # 3
-1500 | -1000 | -4500 | -1000 | # 4
-1000 | NaN | -3000 | -2000 | # 5
NaN | -1500 | -3000 | -3000 | # 6
-1500 | -1000 | -1500 | -2000 | # 7
-1000 | -1000 | -1500 | -2000 | # 8
-1000 | -500 | -3000 | -1000 | # 9
-500 | -1000 | -4500 | -2000 | # 10
Well not drilled yet
Well present but not pumping

## Slide 28: Conclusion → Why Use Integrated Hydrologic Modeling (viz. MF-OWHM)?
Integrated Hydrologic Model → Physically-Based & fully coupled simulation of water from Surface Water, Groundwater, & Landscape
Conjunctive Use Supply-and-Demand Modeling Framework → Connected to Natural and Human Uses & Movement of Water
OWHM’s Mission → Simulates All the Water – All the Time – Everywhere in the Simulated Hydrosphere
Directly Addresses the Supply & Demand Components and interchanges of Conjunctive Use → Supply Constrained & Demand Driven Use and Movement (Flows) of Water throughout the Hydrosphere in a physically-based framework
MF-OWHM is the most complete, advanced, and fastest version of MODFLOW that includes all of the features/options needed for analysis with one model.

## Slide 29: Obtaining MODFLOW-OWHM
Internet Search Engines are your friend ;)
Official Site:
  http://water.usgs.gov/ogw/modflow-owhm/
Unofficial Site:
  https://sourceforge.net/projects/modflow-owhm/
Online Guide:
  http://water.usgs.gov/ogw/modflow-owhm/Guide/index.html
Model Muse for MF-OWHM:
  http://water.usgs.gov/nrp/gwsoftware/ModelMuse/ModelMuse.html
Notes: Personally I still use Lycos

## Slide 30
Thank You
We encourage that you come and talk with us
Future collaboration and incorporation of future ideas
Get on our mailing list for new of updates and innovations
Come to one of our CWEMF Classes
For the Experience of a Lifetime!

## Slide 31: Obtaining MODFLOW-OWHM
Scott E. Boyce and Randall T. Hanson
modflow_owhm@usgs.gov
Official Site:
  http://water.usgs.gov/ogw/modflow-owhm/
Unofficial Site:
  https://sourceforge.net/projects/modflow-owhm/
Online Guide:
  http://water.usgs.gov/ogw/modflow-owhm/Guide/index.html
Model Muse for MF-OWHM:
  http://water.usgs.gov/nrp/gwsoftware/ModelMuse/ModelMuse.html
Notes: Personally I still use Lycos

## Slide 32
Spatial Distribution of
Farm Irrigation Demand and
Water Supply
Predevelopment State (Farm Demand)
Routed Surface-Water Delivery
Non-Routed Deliveries
Groundwater Pumpage
Streamflow Conveyance Network
Theory Farm Mass Balance in FMP
Qgw
Qineff
Qp
Qet
Qsw
FARM MASS BALANCE:
Farm Inflow – Farm Outflows
= Change in Farm Water Storage
Qp + Qsw + Qgw – Qet – Qineff
= dSfarm/dt = 0 (in FMP1)